## Slide 1: Biomass Cookstove Optimization Tool
Liam Cassidy

## Slide 2: Overview
Project Motivation
Background
Research Gap
Theory
Software Details
Preliminary Results
Conclusions
Future Work
Questions

## Slide 3: Project Motivation—Global Significance
Population Significance: In 2010, over 2.4 billion rely on biomass to fuel household cooking and heating1.
Health Significance: Nearly 4 million premature deaths annually1.
Environmental Significance: Black Carbon, CH4, CO and CO2 emissions contribute to climate change2.
[1] MacCarty, N., Bryden, K., Modeling of household Biomass cookstoves: A review. June 2015
[2] Clean Cooking Alliance, Climate and Environment, 2018.
Indoor Air Pollution2

## Slide 4: Project Motivation—Cookstove Industry
Current Goals: Design affordable cleaner burning cookstoves
Current Methods: Mostly experimental
  Problems: time consuming, expensive, limited impact.
  Solution: Computational modelling
Instrumented Cookstove3
[3] Erin Pfieffer, Oregon State University, 2018

## Slide 5: Background
Existing CFD modelling:
  Posner et al. Steady State, 2D, forced draft CFD model of single cookstove geometry4.
  Miller-Loinberg fine resolution transient, 3D, natural draft CFD model of single cookstove geometry5.
[4] Posner, Jonathon D., Multidisciplinary Design of an Innovative Natural Draft, Forced Diffusion Cookstove for Woody and Herbaceous Biomass Fuels in East Africa., University of Washington, September 2018.
[5] Miller-Loinberg, D., A Fine Resolution CFD Simulation Approach for Biomass Cook Dtove Development., Colorado State University, Spring 2011.
Out of Context Contour Plots4

## Slide 6: Research Gap
No existing user-friendly modelling software for cookstove designers.
Current investigations are limited to single cookstove geometries.
Proposed Solution: Develop user-friendly software for cookstove CFD simulation with optimization functionality. Allow users to analyze any geometry based on a variety of input parameters.
Software Development

## Slide 7: Theory—CFD Models
2-dimensional domain:
  Mesh details from Ubuntu command line
Transient simulation:
Reaction Model:
  Adapted from reactingFoam solver
  Compressible
  Chemistry (single reaction)
  Combustion
  Turbulence
  Heat Transfer
  *Details in appendix*

## Slide 8: Software—Overview
Windows OS, programmed in Python using Spyder IDE.
Dependencies:
  Python (V 2.7 or greater), OpenFOAM (V6), Linux subsystem
General Flow:

## Slide 9: Software—User Inputs
Geometric Parameters:
  Combustion chamber diameter (dc)
  Combustion chamber height (hc)
  Height of secondary inlet (hFD)
  Diameter of secondary inlet (dFD)
  Channel width (wch)
  Channel height (hch)
  Cone Deck height(hcd)
  Cone deck length (Lcd)
  Pot spacing (psp)
Flow Parameters:
  Secondary inlet flow rate (QFD)
LC make a figure with the variables

## Slide 10: Software—Modules
Import_geometry:
  Imports geometry from user definition, converts to strings compatible with OpenFOAM convention
create_blockmeshfile:
  Writes the geometry and mesh assignment to blockMeshDict file
setup_surrounding_cases:
  Creates four new cases (varying flow rate) around the user defined flow rate (25-150% user defined flow rate). Writes initial conditions, solver, and control files for each
runner:
  Automate meshing and simulations in parallel.
  Still in development
post_processor:
  Reads data from OpenFOAM outfiles
  Computes maximum average pot temperature as metric for optimization
  Creates four new cases surrounding the optimal case from the previous five simulations
review this to make sure it flows well and makes some sense

## Slide 11: Software—Optimization Details
Single variable optimization.
  Design variable: Secondary air flow rate
  Objective function: Average cookpot temperature
  Direct method: only using objective function values to guide search
  Closest algorithm called “exhaustive search method”

## Slide 12: Software—Optimization Example
--LC make a little excel sheet to compute values of a function with known amplitude/frequency relationship
  ---maybe just use a random Gaussian bell curve for a simple example

## Slide 13: Preliminary Results
Flow Input:

## Slide 14: Conclusions

## Slide 15: Future Work
Reduce Runtime:
  Convert CFD to Axisymmetric
  Auto-runner
Improve Optimization Algorithm:
  Multi-variable
  Gradient based methods
  Alternative methods: Genetic Algorithm
Improve User Friendliness:
Improve Physical Relevance:

## Slide 16: Questions

## Slide 17: References
Department of Mechanical Engineering, Indian Institute of Technology Madras., Optimization Algorithms. URL: https://mech.iitm.ac.in/meiitm/

## Slide 18: Appendix

## Slide 19: Appendix